## Slide 1: InfiniBand

## Slide 2
Overview
  What is InfiniBand
  InfiniBand Architecture

## Slide 3: IBA
The InfiniBand Architecture (IBA) is a new industry-standard architecture for server I/O and inter-server communication.
  Developed by InfiniBand Trade Association (IBTA).
It defines a switch-based, point-to-point interconnection network that enables
  High-speed
  Low-latency
  communication between connected devices.

## Slide 4: InfiniBand Devices
Adapter Card
Cable
Switch

## Slide 5: Usage
InfiniBand is commonly used in high performance computing (HPC).
InfiniBand 44.80%
Gigabit Ethernet
37.80%

## Slide 6: InfiniBand VS. Ethernet
 | Ethernet | InfiniBand
Commonly used in what kinds of network | Local area network(LAN) or wide area network(WAN) | Interprocess communication (IPC) network
Transmission medium | Copper/optical | Copper/optical
Bandwidth | 1Gb/10Gb | 2.5Gb~120Gb
Latency | High | Low
Popularity | High | Low
Cost | Low | High

## Slide 7: InfiniBand Architecture
The IBA Subnet
Communication Service
Communication Model
Subnet Management

## Slide 8: IBA Subnet Overview
IBA subnet is the smallest complete IBA unit.
  Usually used for system area network.
Element of a subnet
  Endnodes
  Links
  Channel Adapters(CAs)
    Connect end nodes to links
  Switches
  Subnet manager

## Slide 9: IBA Subnet

## Slide 10: Endnodes
IBA endnodes are the ultimate sources and sinks of communication in IBA.
  They may be host systems or devices.
    Ex. network adapters, storage subsystems, etc.

## Slide 11: Links
IBA links are bidirectional point-to-point communication channels, and may be either copper and optical fibre.
  Link widths are 1X, 4X, and 12X.

## Slide 12: Channel Adapter
Channel Adapter (CA) is the interface between an endnode and a link
There are two types of channel adapters
  Host channel adapter(HCA)
    For inter-server communication
    Has a collection of features that are defined to be available to host programs, defined by verbs
  Target channel adapter(TCA)
    For server IO communication
    No defined software interface

## Slide 13: Switches
IBA switches route messages from their source to their destination based on routing tables
  Support multicast and multiple virtual lanes
Switch size denotes the number of ports
  The maximum switch size supported is one with 256 ports
The addressing used by switched
  Local Identifiers, or LIDs allows 48K end nodes on a single subnet
  The 64K LID address space is reserved for multicast addresses
  Routing between different subnets is done on the basis of a Global Identifier (GID) that is 128 bits long

## Slide 14: Addressing
LIDs
  Local Identifiers, 16 bits
  Used within a subnet by switch for routing
GUIDs (For each HCA)
  Global Unique Identifier
  64 EUI-64 IEEE-defined identifiers for elements in a subnet
GIDs
  Global IDs, 128 bits
  Used for routing across subnets

## Slide 15: Infiniband Components
HCA
Switch
Router
Gateway (Infiniband to Ethernet)

## Slide 16: HCA
GUID (Global Unique Identifier) = 64 bits (Like Ethernet Mac Address)
Assigned by IB vendor
Persistent (Reboots)
Each switch will have one GUID
Chassis switch will allow to combine multiple GUID into one

## Slide 17: LID (Local Identifier)
16 bit
By Subnet Manager
Not persistent
LID RANGE
0x0000 = Reserved
0x0001 <-> 0xBFFF Unicast
0xc001 <-> 0xFFFE Multicast
0xFFFF = Reserved

## Slide 18: GID (Global Identifier)
128 bit field in Global Routing Header used to route packets between different IB subnets
Port ID Guid + Subent Id (Link Local)

## Slide 19: Subnet Manager
Each node will have a agent
Agent always in touch with SM
Management Datagram (Standard Message format for Agent-Manager communication)
Subnet Packet Manager ( Manager-Agent Communication)
Each Communication medium will have virtual lanes
VL-15 (Traffic to SM)
VL- (0-7) used for data traffic
OPED (InfiniBand Driver) Open Fabrics Enterprise Distribution

## Slide 21
LRH = 8 bytes
GRH = 40 bytes
IBH = 12 bytes
Payload = 4096 bytes
I-CRC = 4 bytes
V-CRC = 2 bytes

## Slide 22: InfiniBand Architecture
The IBA Subnet
Communication Service
Communication Model
Subnet Management

## Slide 23: Communication Service Types

## Slide 24: Data Rate
Effective theoretical throughput

## Slide 25: InfiniBand Architecture
The IBA Subnet
Communication Service
Communication Model
Subnet Management

## Slide 26: Queue-Based Model
Channel adapters communicate using Work Queues of three types:
  Queue Pair(QP) consists of
    Send queue
    Receive queue
  Work Queue Request (WQR) contains the communication instruction
    It would be submitted to QP.
  Completion Queues (CQs) use Completion Queue Entries (CQEs) to report the completion of the communication

## Slide 27: Queue-Based Mode

## Slide 28: Communication Semantics
Two types of communication semantics
  Channel semantics
    With traditional send/receive operations.
  Memory semantics
    With RDMA operations.

## Slide 29: Send and Receive
Transport Engine
Channel
Adapter
QP
Send Recv
CQ
Port
Transport Engine
Channel
Adapter
QP
Send Recv
CQ
Port
Remote Process
Process
Fabric
WQE

## Slide 30: Send and Receive
Transport Engine
Channel
Adapter
QP
Send Recv
CQ
Port
Transport Engine
Channel
Adapter
QP
Send Recv
CQ
Port
Remote Process
Process
WQE
Fabric
WQE

## Slide 31: Send and Receive
Transport Engine
Channel
Adapter
QP
Send Recv
CQ
Port
Transport Engine
Channel
Adapter
QP
Send Recv
CQ
Port
WQE
Remote Process
Process
Fabric
WQE
Data packet

## Slide 32: Send and Receive
Remote Process
Process
Transport Engine
Channel
Adapter
QP
Send Recv
CQ
Port
Transport Engine
Channel
Adapter
QP
Send Recv
CQ
Port
Complete
CQE
CQE
Fabric

## Slide 33: RDMA Read / Write
Transport Engine
Channel
Adapter
QP
Send Recv
CQ
Port
Transport Engine
Channel
Adapter
QP
Send Recv
CQ
Port
Remote Process
Process
Fabric
Target Buffer

## Slide 34: RDMA Read / Write
Transport Engine
Channel
Adapter
QP
Send Recv
CQ
Port
Transport Engine
Channel
Adapter
QP
Send Recv
CQ
Port
Remote Process
Process
WQE
Fabric
Target Buffer

## Slide 35: RDMA Read / Write
Transport Engine
Channel
Adapter
QP
Send Recv
CQ
Port
Transport Engine
Channel
Adapter
QP
Send Recv
CQ
Port
WQE
Remote Process
Process
Fabric
Data packet
Target Buffer
Read / Write

## Slide 36: RDMA Read / Write
Transport Engine
Channel
Adapter
QP
Send Recv
CQ
Port
Transport Engine
Channel
Adapter
QP
Send Recv
CQ
Port
Remote Process
Process
Complete
CQE
Fabric
Target Buffer