## Slide 1: Interconnection Networks: Introduction
B S V Ramesh
Notes: (some adapted from Interconnection Networks Computer Architecture: A Quantitative Approach 4th Edition, Appendix E, Timothy Pinkston and Jose Duato)

## Slide 2: Introduction
How to connect individual devices into a group of communicating devices?
  A device can be:
    Component within a chip
    Component within a computer
    Computer
    System of computers
  Network consists of:
    End point devices with interface to network
    Links
    Interconnect hardware
Goal: transfer maximum amount of information with the least cost (minimum time, power)

## Slide 3
Infiniband architecture overview
  Components:
    Links
    Channel adaptors
    Switches
    Routers
  The specification allows Infiniband wide area network, but mostly adopted as a system/storage area network.
  Topology:
    Irregular
    Regular: Fat tree , hypercube, torus, etc.

## Slide 4
  Link speed (signal rate):
    Single data rate (SDR): 2.5Gbps (1X), 10Gbps (4X), and 30Gbps (12X).
    Double data rate (DDR): 5Gbps (1X), 20 Gbps (4X), 60Gbps(12X)
    Quad data rate (QDR): 10Gbps (1X), 40Gbps(4X), 120Gbps(12X)
    Fourteen data rate (FDR): 14Gbps(1X), 56Gbps(4X), 168Gbps(12X)
    Enhanced data rate (EDR): 25Gbps(1X), 100Gbps(4X), 300Gbps(12X)

## Slide 5: What InfiniBand Offers
Lowest Layer for scalable IO interconnect
High-Performance
Low Latency
Reliable Switch Fabric
Offers higher layers of functionality
Application Clustering
Fast Inter Process Communications
Storage Area Networks

## Slide 6
Layers: somewhat similar to TCP/IP
  Physical layer
  Link layer
    Error detection (CRC checksum)
    flow control (credit based)
    switching, virtual lanes (VL),
    forwarding table computed by subnet manager
      Single path deterministic routing (not adaptive)
  Network layer: across subnets.
    No use for the cluster environment
  Transport layer
    Reliable/unreliable, connection/datagram
  Verbs: interface between adaptors and OS/Users

## Slide 7: Interconnection Networks
System/Storage Area Network (SANs)
  Multiprocessor and multicomputer systems
    Interprocessor and processor-memory interconnections
  Server and data center environments
    Storage and I/O components
  Hundreds to thousands of devices interconnected
    IBM Blue Gene/L supercomputer (64K nodes, each with 2 processors)
  Maximum interconnect distance typically on the order of tens of meters, but some with as high as a few hundred meters
    InfiniBand: 120 Gbps over a distance of 300 m
  Examples (standards and proprietary)
    InfiniBand, Myrinet, Quadrics, Advanced Switching Interconnect